## Slide 1: Hematology specimen acceptability
Dr Ali Maleki PhD in Lab Hematology & Transfusion Sciences
Clinical Lab Sciences Department
School of Paramedical Sciences
Kermanshah University of Medical Sciences
Ali.maleki@kums.ac.ir

## Slide 2
Hematology specimen acceptability

## Slide 4
Although Lab medicine seems overall less vulnerable to mistakes than other clinical and diagnostic areas  the chance of errors is still not negligible and may generate adverse consequences on both the quality of testing and patient safety.
Lab errors in total testing process (TTP):
  preanalytical errors  the majority of the total errors (46 - 68%) in Lab medicine  mainly emerging from manually intensive activities (collection, handling, transportation, preparation and storage of specimens)
  errors occur in the analytical (7 - 13%)
  errors occur in the postanalytical (18 -47%) phase
Laboratories usually establish a guideline for evaluating the acceptance of specimens  specimens not meeting the criteria of acceptability are rejected.
Intoduction

## Slide 5
Preanalytical errors  start at the point of test requests by clinicians
Studies showed that  the main rejection reasons for hematology specimens were clotted samples and insufficient specimen quantity (5,10).
  Personal impact on specimen collection was an important factor
    preanalytical error rate was 2-4 times higher for non-Lab phlebotomists than Lab staff (4).
The aim of this study was  to determine:
  the frequency and reasons for rejected hematology specimens,
  preanalytical variables which may affect specimen quality, and
  consequences of rejection,
  provide suggestions on monitoring quality indicators as to obtain a quality improvement.
Intoduction

## Slide 6
Materials and methods
A cross-sectional survey was conducted and a questionnaire was sent to 1586 Labs.
Participants were asked to provide general information about institution and practices on specimen management and record rejections and reasons for rejection from 1st to 31st July.
The questionnaire was divided into 2 parts:
The first part contained 18 questions on institution characteristics and Lab practices on collection, transportation, and specimen handling.
The second part comprised information about hematology specimen acceptability

## Slide 7
For each rejected specimen, the following information had to be recorded:
  source department,
  container type,
  container material type,
  transportation method,
  phlebotomy personnel,
  reason for rejection,
  action taken
  time (including time of specimen receipt, time of specimen rejection and time of specimen recollected or relabelled).
Materials and methods

## Slide 8
Participants also provided the:
  total number of hematology specimens (both acceptable for testing and rejected)
  the total number of specimens by source department,
  container type,
  container material type,
  transportation method
  phlebotomy personnel
Materials and methods

## Slide 9
Excel (2007 version) and SPSS 20.0 were used to analyse collected data.
The overall rejection rate and interLab rejection rate were calculated
Percentage (%) and sigma value (σ) were employed  to evaluate the status of rejection rate
The characteristics and practices of institutions were considered and participants were grouped according to them.
The Odds ratio (OR) was calculated, for each level
Nonparametric Kruskal-Wallis test for  3 groups and Mann-Whitney U test for 2 groups were performed to compare the interLab rejection rate
  Significance was defined as probability, P-value＜0.05.
Statistical analysis

## Slide 10
A total of 1586 questionnaires were sent  890 (56%) questionnaires were returned
  According to exclusion criteria  580 questionnaires were considered valid and included in further analysis.
Most of participants (69%) were general hospitals and 15% were specialized hospitals.
Results

## Slide 11
Nurse managed by nursing department was the most frequent phlebotomy personnel in:
  inpatient department (97%) and
  emergency department (72%)
for outpatient department, the common phlebotomy personnel were:
  nurse managed by nursing department (39%),
  Lab personnel (34%) and
  nurse managed by clinical Lab (26%)
Results

## Slide 12
Common specimen transportation methods were by:
  in inpatient department  full-time transportation worker (67%) and nurse (12%)
  in outpatient department  full-time transportation worker (32%) and Lab personnel (44%)
  in emergency department  full-time transportation worker (45%) and nurse (22%)
Results

## Slide 13







## Slide 14





## Slide 15







## Slide 16





## Slide 17





## Slide 18
Table 2 illustrates the specimen rejection rate according to Lab characteristics/practices, including:
  hospital grade, bed size, ISO 15189/CAP accreditation,
  training frequency for phlebotomy personnel,
  specimen rejection criteria, and
  periodically reviewed main reasons for rejection and take measures
Results

## Slide 20
Table 3 compares % of collected & rejected specimens according to specimen characteristics
  87% of rejection specimens were from inpatient department, with a rejection rate of 0.19%

## Slide 21
Table 3 compares continued …

## Slide 22
Table 4 illustrates the distribution of rejected specimens, based on reasons for rejection
~85% of rejections attributed to 5 reasons:
  specimen clotted (57%),
  insufficient specimen volume (14%),
  inappropriate specimen anticoagulant volume ratio (6.9%),
  incorrect container type (4.2%)
  inadequately labelled (2.9%)
Results

## Slide 23
The rejection rate in the study was similar to, but slightly lower than that found in the previous CBC testing study in 2012 (11).
  11. Zhang L, Yang X, Wang W, Wang ZG. National survey on specimen acceptability for CBC testing of clinical laboratories in China. Int J Lab Hematol. 2016;38:e48-e51.
The comparison  laboratories in China pay more attention to collection and reception of specimens in the past 5 years  a  in rejection due to preanalytical errors.
Discussion

## Slide 24
Compared with the study by CAP and in Spain  the overall rejection rate in this study was much lower (3,5,7)
  3. Jones BA, Calam RR, Howanitz PJ. Chemistry specimen acceptability: A College of American Pathologists Q-Probes Study of 453 Laboratories. Arch Pathol Lab Med.26-121:19;197.
  5. Jones BA, Meier F, Howanitz PJ. CBC specimen acceptability: A College of American Pathologists Q-Probes Study of 703 Laboratories. Arch Pathol Lab Med.8-119:203;1995.
  7. Alsina MJ, Alvarez V, Barba N, Bullich S, Cortes M, Escoda I, Martinez-Bru C. Preanalytical quality control program - an overview of results (2001-2005 summary). Clin Chem Lab Med. 2008;46:849-54.
Discussion

## Slide 25
The most common rejection reason was clotted specimen  occurred 4 times > the second most common reason for rejection (insufficient specimen volume)
  The result was similar to the study of hematology specimen acceptability conducted by CAP (5).
    5. Jones BA, Meier F, Howanitz PJ. CBC specimen acceptability: A College of American Pathologists Q-Probes Study of 703 Laboratories. Arch Pathol Lab Med.8-119:203;1995.
Since the predominance of clotted specimens  participants were suggested to have an investigation for reasons for that. For example, the blood collection procedure and the mixing procedure of collection tube   occurrence of clotted specimen.
Discussion

## Slide 26
Transportation method and phlebotomy personnel  were important influence factors for specimen acceptability.
  Specimens transported by Lab personnel and specimens collected by Lab personnel and nurse managed by Lab exhibited a much lower rejection rate.
    It possibly because Lab personnel had a better knowledge of the influence factors of specimen and had a better practice on specimen collection and transportation.
Discussion

## Slide 27
The common consequences of specimen rejection were  the need to recollect a new specimen  delay in examination & reporting
The outcomes of specimen recollection and delay in reporting  led to patient complaint and dissatisfaction and postponed the diagnosis and treatment for the patient.
However, there was certain limitation in the study.
  Participants were asked to register all the information of rejected specimens  which was hard to complete.
Discussion

## Slide 28
In summary,
the management of unacceptable specimens in China needs to be improved.
The criteria for specimen rejection and judgment method for unacceptable specimens  need to be harmonized.
Specimen rejection rate is an important indicator for quality monitoring in preanalytical phase.
Laboratories should regularly review the monthly specimen rejection rate and related influence factor  and take effective actions.
Discussion

## Slide 29
Thanks for your attention